## Slide 1: EASy Connectivity Verification EDCS- ... (based on EASy Template EDCS-764298) [Date – Location]
Joe Clarke
Customer Support Engineer
jclarke@cisco.com
http://wikicentral.cisco.com/confluence/display/PROJECT/Embedded+Automation+Systems+(EASy)
Internal Alias: easy@cisco.com
External Alias: ask-easy@cisco.com
Gloria Turner
Technical Marketing Engineer
glturner@cisco.com
Notes: <number>

## Slide 2
Objective
Connectivity Verification
Notes: <number>

## Slide 3: EASy Objective: Connectivity Verification
See: http://www.cisco.com/en/US/docs/ios/ipsla/configuration/guide/12_4t/sla_12_4t_book.html
Solution: Use IP SLA with Enhanced Object Tracking and the Embedded Event Manager to test network connectivity. Fail over to a redundant interface when the primary network no longer passes traffic.
Problem: Be able to detect loss of network connectivity and fail over to the secondary interface

## Slide 4: EASy Overview
Application or Service | High Availability
Technology | IP SLA, Enhanced Object Tracking
Problem | The primary network may go down without taking down the local interface. You need to be able to detect when the network is no longer capable of passing traffic, and fail over to a secondary interface.
Impact | Network Availability
Non-EASy Solution | IP SLA and enhanced object tracking Pros: IOS configuration only, no script required Cons: Secondary interface needs to be permanenetly up and backup route triggered by routing statements. Limited commands available to bring up secondary interface, to control timing, and to notify users of such event
Benefit of EASy Solution | Ensures high network availability with configurable actions upon the detection of a failed primary network
Status | Deliverable in Development
Category | Network Management – Capacity Planning – Routing – QoS – High Availability – User Interface – Diagnostics – Security
Notes: <number>

## Slide 5: EASy Background
X
HQ
1. Primary connection is established
2. Primary path is down
3. Connectivity Verification EEM script detects the failed primary path
Remote Office
4. Connectivity Verification EEM script brings up the backup interface, passing traffic via secondary path
Notes: <number>

## Slide 6
Pseudo Code
Connectivity Verification
Notes: <number>

## Slide 7: EASy Pseudo Code: Connectivity Verification Script
Did IP SLA
operation time out?
No
Yes
Tracked object is down,
execute configured
down commands
Send down syslog
Is down-syslog
Configured?
Track object is up,
Connectivity is ok
Did IP SLA
Operation
Complete
Successfully?
Yes
No
Yes
Tracked object is up,
execute configured up
commands
No
Is up-syslog
Configured?
Send up syslog
Yes
No
Notes: <number>
Hi Paul, Always a challenging question for us in TAC... :) check the Table 13 under http://www.cisco.com/en/US/docs/ios/12_4t/release/notes/124TNEWF.html#wp30520 there is a mapping on the deprecated mibs. ...If you don´t find specific values for the mapping, Expression-MIB might be the key in combination with TCL/EEM, before EEM 3.1 is available. But you will need to check before if Expression-MIB/RFC2982-MIB is supported in the image running in your cat4506 I´ve uploaded in Cisco Beyond two TCL policies, for this, under Network Management Category. One for the CLI Expression-MIB implementation, and the other one based on snmp commands implementation... The scripts are specifically built on RFC2982-MIB, which is the latest implementation for the Expression-MIB in CiscoDevices. Expression-MIB was based on the oid tree 1.3.6.1.4.1.9.10.22 RFC2982-MIB is based on the oid tree 1.3.6.1.2.1.90
.1.3.6.1.4.1.9.10.22 expressionMIB OBJECT-TYPE -- FROM EXPRESSION-MIB DESCRIPTION "The MIB module for defining expressions of MIB objects for network management purposes. This MIB is a work in progress of the IETF Distributed Management working group and is subject to change by that body." ::= { iso(1) org(3) dod(6) internet(1) private(4) enterprises(1) cisco(9) ciscoExperiment(10) 22 }
RFC2982 implementation
Anirban Karmakar (5:44:28 PM): CSCsg25646 is the DDTS
Marisol Palmero Amador (5:44:47 PM): great
Marisol Palmero Amador (5:45:02 PM): I can take the informatoin from there
Anirban Karmakar (5:45:18 PM): okay
Marisol Palmero Amador (5:45:30 PM): thanks
Anirban Karmakar (5:45:38 PM): do u need the EC slide
Marisol Palmero Amador (5:46:02 PM): that will be great!
Anirban Karmakar (5:46:10 PM): EDCS-528800
Marisol Palmero Amador (5:46:14 PM): thanks

## Slide 8: EASy Pseudo Code: Core Script
set prio_array(emergencies) "emerg"
set prio_array(alerts) "alert"
set prio_array(critical) "crit"
set prio_array(errors) "err"
set prio_array(warnings) "warning"
set prio_array(notifications) "notice"
set prio_array(informational) "info"
set prio_array(debugging) "debug"
if { [catch { set prev_state [context_retrieve EASYIPSLACTXT prev_state] } errmsg] } {
set prev_state "Up"
}
set output [run_cli [list "show track $easy_ipsla_track_idx | incl Reachability is"]]
if { $output == "" } {
action_syslog priority err msg "ERROR: Did not get output from 'show track $easy_ipsla_track_idx | incl Reachability is'"
return -code ok
}
if { ! [regexp {Reachability is (\w+)} $output -> status] } {
action_syslog priority err msg "ERROR: Output from 'show track $easy_ipsla_track_idx | incl Reachability is' is not in expected format (output = '$output')"
return -code ok
}
if { $status == $prev_state } {
set prev_state $status
catch { context_save EASYIPSLACTXT prev_state } errmsg
return -code ok
}
Retrieve previously saved
state.
Obtain the current
state from the
output of “show
track”.
If the current state is
the same as the previous
state, just exit.

## Slide 9: EASy Pseudo Code: Core Script
set cmds $easy_ipsla_down_cmds
set slg $easy_ipsla_down_syslog
set prio $prio_array($easy_ipsla_down_slg_prio)
if { $status == "Up" } {
set cmds $easy_ipsla_up_cmds
set slg $easy_ipsla_up_syslog
set prio $prio_array($easy_ipsla_down_slg_prio)
}
set cout ""
if { [catch {run_cli [split $cmds ";"]} result] } {
set cout "Failed to run commands: '$result'"
} else {
set cout $result
}
if { $slg != "" } {
append slg " (cmd output: $cout)"
action_syslog priority $prio msg $slg
}
set prev_state $status
catch { context_save EASYIPSLACTXT prev_state } errmsg
Determine the correct
command set to run based
on the current tracked
object state
The commands are separated by
‘;’, so split them out, and
run them.
Send a syslog message is
required, and append any
output from the configured
commands.
Finally, save the current
state, and exit.

## Slide 10
EASy Deliverable
Connectivity Verification Overview of Components
Notes: <number>

## Slide 11: EASy Components: Connectivity Verification
Event Detector
Status of the tracked object configured by the user
EEM Actions
Configurable actions using IOS CLI commands
EEM Outputs (optional)
Configurable syslog messages notifying events
Notes: <number>
Here is a working example how we did it:
It is really a Use case of what it is already implemented today in IOS, I´m combining EEM in this case, in the way to extract this value every 60 sec., but this could be a pure TCL script as well...
The value that I am extracting with a regular expression in this specific example is "packets input" counter for Interface FastEthernet0/0, which is the value assigned to the Expression MIB variable that I build(exp5)
You will be able to see that every 60 sec the expression, called exp5, is updated, and the possibility to extract this value via SNMP.
Here is the cli output of the value I would like to collect via snmp: dehors#sh int fastEther0/0 | inc packets input 305741 packets input, 35322041 bytes
The regular expression will be: .([0-9]+).*packets input apply to the command "show interface fastethernet0/0"
The only prerequisite here will be the support for Expression-MIB and TCL. For simplicity, this example is running in 12.4(20)T.
A modification on the script should be done for previous ios releases, not supporting Expression-MIB and CLI combination. In that case we will need to use pure snmpset within TCL for the Expression-MIB variables.
Making use of Environment variables in EEM, things are getting even more modular, as we will not even have to change the TCL policy, we can configure: >frecuency, >show command, >regular expression and >even body of the syslog message to send once the TCL policy runs (optional)
In this example: event manager environment SR_000000549_countdown_entry 60 event manager environment SR_000000549_match_cmd show interface fastethernet0/0 event manager environment SR_000000549_match_pattern .([0-9]+).*packets input event manager environment SR_000000549_nok_msg it works
Each time that the script is executed, the counter for which the match occurs is getting updated under the expression configured, the ED in this case is count down timer, as already mentioned, to be executed every 60 sec:
dehors# *Dec 20 12:18:39.816: %SYS-5-CONFIG_I: Configured from console by vty0 *Dec 20 2008 12:18:39.816 UTC: %HA_EM-6-LOG: SR_000000549-script.tcl: it works *Dec 20 12:18:40.664: %SYS-5-CONFIG_I: Configured from console by vty1 dehors# dehors#sh run | beg expression >>>>>>>>>>< (extracting the expression CLI) ... snmp mib expression owner marisol name exp5 expression 305547 !
....
dehors# *Dec 20 12:19:39.532: %SYS-5-CONFIG_I: Configured from console by vty0 *Dec 20 2008 12:19:39.532 UTC: %HA_EM-6-LOG: SR_000000549-script.tcl: it works *Dec 20 12:19:40.376: %SYS-5-CONFIG_I: Configured from console by vty1 dehors#sh run | beg expression >>>>>>>>>>< (extracting the expression via CLI) ... snmp mib expression owner marisol name exp5 expression 305627 ! .... *Dec 20 12:20:39.532: %SYS-5-CONFIG_I: Configured from console by vty0 *Dec 20 2008 12:20:39.532 UTC: %HA_EM-6-LOG: SR_000000549-script.tcl: it works *Dec 20 12:20:40.372: %SYS-5-CONFIG_I: Configured from conso! 1 line con 0 line aux 0
dehors#sh run | beg expression >>>>>>>>>>< (extracting the expression via CLI) snmp mib expression owner marisol name exp5 expression 305741 ! .... ! -More- *Dec 20 12:21:39.524: %SYS-5-CONFIG_I: Configured from console by vty0 *Dec 20 2008 12:21:39.524 UTC: %HA_EM-6-LOG: SR_000000549-script.tcl: it works *Dec 20 12:21:40.368: %SYS-5-CONFIG_I: Configured from console by vty1 *Dec 20 12:22:39.532: %SYS-5-CONFIG_I: Configured from console by vty0 *Dec 20 2008 12:22:39.532 UTC: %HA_EM-6-LOG: SR_000000549-script.tcl: it works *Dec 20 12:22:40.380: %SYS-5-CONFIG_I: Configured from console by vty1 *Dec 20 12:23:39.536: %SYS-5-CONFIG_I: Configured from console by vty0 *Dec 20 2008 12:23:39.536 UTC: %HA_EM-6-LOG: SR_000000549-script.tcl: it works *Dec 20 12:23:40.380: %SYS-5-CONFIG_I: Configured from conso! 1 line con 0
You can see that the counter under expression called exp5 is updated!
And to extract the value via snmp, you poll expExpressionEntry, and specifically the Expression value that in this case is expExpression(3). The indexes are expExpressionOwner (109.97.114.105.115.111.108 - marisol) and expExpressionName (101.120.112.53 - exp5):
mpalmero@sweet-brew-6% snmpwalk -c public -v 2c dehors 1.3.6.1.2.1.90 | grep 53 SNMPv2-SMI::mib-2.90.1.2.1.1.3.7.109.97.114.105.115.111.108.4.101.120.112.53 = STRING: "305741" <<<<<<<<<<<<<<<<<<<<<<<<<<<<<< SNMPv2-SMI::mib-2.90.1.2.1.1.4.7.109.97.114.105.115.111.108.4.101.120.112.53 = INTEGER: 1 SNMPv2-SMI::mib-2.90.1.2.1.1.5.7.109.97.114.105.115.111.108.4.101.120.112.53 = "" SNMPv2-SMI::mib-2.90.1.2.1.1.6.7.109.97.114.105.115.111.108.4.101.120.112.53 = INTEGER: 0 SNMPv2-SMI::mib-2.90.1.2.1.1.7.7.109.97.114.105.115.111.108.4.101.120.112.53 = OID: SNMPv2-SMI::zeroDotZero SNMPv2-SMI::mib-2.90.1.2.1.1.8.7.109.97.114.105.115.111.108.4.101.120.112.53 = Counter32: 0 SNMPv2-SMI::mib-2.90.1.2.1.1.9.7.109.97.114.105.115.111.108.4.101.120.112.53 = INTEGER: 2 mpalmero@sweet-brew-6%
The script is running in one of our lab tests at the moment, for any further questions/clarifications!
To build the TCL policy, I´ve used the tool we presented to you in the past, together with Raph Wouters and Aleks Vidakovic, with this we are separating the complexity to build the TCL policy as well: http://superbird/eem_frontend/
The script is under attachments section on this page:
http://zed.cisco.com/confluence/download/attachments/312411301/SR_000000549-script.tcl
enjoy!

## Slide 12: EASy Environment Variables Connectivity Verification
EEM environment variables for the Connectivity Verification Script
easy_ipsla_track_idx : Tracked object ID
easy_ipsla_down_cmds : Semi-colon separated list of commands to run when the tracked object goes down
easy_ipsla_up_cmds : Semi-colon separated list of commands to run when the tracked object comes back up
easy_ipsla_down_syslog : Syslog message to send when the tracked object goes down (or empty for no message)
easy_ipsla_up_syslog : Syslog message to send when the tracked object comes back up (or empty for no message)
easy_ipsla_down_slg_prio : Priority of the syslog message sent when the tracked object goes down
easy_ipsla_up_slg_prio : Priority of the syslog message sent when the tracked object comes back up
Notes: <number>

## Slide 13
EASy Deliverable
Connectivity Verification Installation & Verification
Notes: <number>

## Slide 14: EASy Preparing for Installation
Prerequisites:
- Any IOS based hardware platform with support for EEM, IP SLA and enhanced object
tracking
- easy_installer.tcl script should be copied to router flash
- optional step to copy the package file to router flash.
The package file can remain on a tftp server.
Configuration: - optional CLI configuration to create an alias for the easy_installer.tcl script
EASy Installer: ensure that the EASy Installer is available:
Router#sh run | inc easy
alias exec easy_installer tclsh flash:/easy/easy_installer.tcl
Notes: <number>

## Slide 15: EASy Installing the Package
Router# easy-installer tftp://223.255.254.254/easy/easy-ipsla-tracker.tar
--------------------------------------------------------------------------------
Configure and Install EASy Package 'easy-ipsla-tracker-1.0'
--------------------------------------------------------------------------------
1. Display Package Description
2. Configure Package Parameters
3. Deploy Package Policies
4. Configure IP SLA
5. Exit
Enter option:
Router#sh run | inc easy
alias exec easy_installer tclsh flash:/easy/easy_installer.tcl
Notes: <number>

## Slide 16: EASy Installing the Package – Example
This package provides an EEM solution to watch an IP SLA collector, then
run CLI commands if the collector goes down (and again when the collector
comes back up). This is done via Enhanced Object Tracking.
This package also offers a simple way to configure a new IP SLA collector
(ICMP Echo only) and tracked object if one does not already exist.
Hit enter to continue...
----------------------------------------------------------------------------
IP SLA and Object Tracking Configuration Menu
----------------------------------------------------------------------------
1. Use existing tracked object
2. Configure new IP SLA ICMP echo collector and tracked object
3. Return to main menu
Enter option: 1
Enter ID number of existing tracked object: 1
Enter option: 1 [Display Package Description]
Enter option: 2 [Configure Package Parameters]
!! if you want to change any parameter, you might need to uninstall the package and install it again
Notes: <number>

## Slide 17: EASy Installing the Package – Example
----------------------------------------------------------------------------
IP SLA and Object Tracking Configuration Menu
----------------------------------------------------------------------------
1. Use existing tracked object
2. Configure new IP SLA ICMP echo collector and tracked object
3. Return to main menu
Enter option: 3
Enter the commands you want to run when the IP SLA collector
goes down. Enter each command on a separate line. All
commands will be run in enable mode. Hit enter on a line
by itself to stop entering commands:
config t
interface fastethernet0
no shut
end
Notes: <number>

## Slide 18: EASy Installing the Package – Example
Send syslog message when collector is down (y/n) [y]:
Enter message to send when collector is down: Object unreachable
Enter priority for the down syslog message (one of emergencies, alerts, critical
, errors, warnings, notifications, informational, debugging) [informational]:
Commands:
config t
interface fastethernet0
no shut
end
Syslog message when collector is down : Object unreachable
Syslog priority : informational
Are you satisfied with these settings (y/n) [y]:
Notes: <number>

## Slide 19: EASy Installing the Package – Example
Enter the commands you want to run when the IP SLA collector
comes back up. Enter each command on a separate line. All
commands will be run in enable mode. Hit enter on a line
by itself to stop entering commands:
config t
interface fastethernet0
shut
end
Send syslog message when collector is up (y/n) [y]:
Enter message to send when collector is up: Object reachable
Enter priority for the up syslog message (one of emergencies, alerts, critical,
errors, warnings, notifications, informational, debugging) [informational]:
Commands:
config t
interface fastethernet0
shut
end
Syslog message when collector is up : Object reachable
Syslog priority : informational
Are you satisfied with these settings (y/n) [y]:
Notes: <number>

## Slide 20: EASy Installing the Package – Example
----------------------------------------------------------------
Configure and Install EASy Package 'easy-ipsla-tracker-1.0'
----------------------------------------------------------------
1. Display Package Description
2. Configure Package Parameters
3. Deploy Package Policies
4. Configure IP SLA
5. Exit
Enter option: 3
Specify the directory to store EEM user policies: easy
INFO: Package easy-ipsla-tracker-1.0 successfully installed.
Hit enter to continue...
Enter option: 3 [Deploy Package Policies]
Notes: <number>

## Slide 21: EASy Verifying the Installation
Listing the installed packages
Router#easy_installer --list
EASy packages installed:
easy-ipsla-tracker-1.0 Track an IP SLA operation, and run CLI commands on state changes
Hit enter to continue...
Notes: <number>

## Slide 22: EASy Verifying the Installation
Router# show event manager policy registered
No. Class Type Event Type Trap Time Registered Name
1 applet user track Off Thu Apr 25 05:49:08 2002 easy-
ipsla-down-tracker
track 1 state down
maxrun 20.000
action 1 cli command "enable"
action 2 cli command "config t"
action 3 cli command "interface fastethernet0"
action 4 cli command "no shut"
action 5 cli command "end"
action 6 syslog priority informational msg "Object unreachable (cmd output: $_c
li_result)"
2 applet user track Off Thu Apr 25 05:49:08 2002 easy-
ipsla-up-tracker
track 1 state up
maxrun 20.000
action 1 cli command "enable"
action 2 cli command "config t"
action 3 cli command "interface fastethernet0"
action 4 cli command "shut"
action 5 cli command "end"
action 6 syslog priority informational msg "Object reachable (cmd output: $_cli
_result)"
Verifying Registered Scripts

## Slide 23: EASy De-Installation
Instructions to de-install the package and verify it’s removal:
Router#easy_installer --uninstall --prefix flash:/easy --pkgname easy-ipsla-tracker
Uninstalling easy-ipsla-tracker...DONE!
INFO: Uninstall of easy-ipsla-tracker completed successfully.
Configuration was changed, do you want to save the running config to startup? (y
/n) [y]
Notes: <number>

## Slide 24
EASy Deliverable
Connectivity Verification Operation
Notes: <number>

## Slide 25: EASy During Operation
Simulate loss of primary connection via CLI
Router#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#int vlan 1
Router(config-if)#shut
Router(config-if)#end
Router#
*Apr 25 06:07:54.177: %SYS-5-CONFIG_I: Configured from console by console
*Apr 25 06:07:55.401: %LINK-5-CHANGED: Interface Vlan1, changed state to adminis
tratively down
*Apr 25 06:07:56.401: %LINEPROTO-5-UPDOWN: Line protocol on Interface Vlan1, cha
nged state to down
Router#
*Apr 25 06:08:03.117: %TRACKING-5-STATE: 1 ip sla 1 reachability Up->Down
*Apr 25 06:08:03.193: %SYS-5-CONFIG_I: Configured from console by on vty0 (EEM:
easy-ipsla-down-tracker)
*Apr 25 06:08:03.201: %HA_EM-6-LOG: easy-ipsla-down-tracker: Object unreachable
(cmd output:
Router#)
Router#
Notes: <number>

## Slide 26: EASy During Operation
Simulate recovery of primary connection via CLI
Router#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#int vlan 1
Router(config-if)#no shut
Router(config-if)#end
Router#
Router#
*Apr 25 06:11:47.773: %SYS-5-CONFIG_I: Configured from console by console
*Apr 25 06:11:49.317: %LINK-3-UPDOWN: Interface Vlan1, changed state to up
*Apr 25 06:11:50.317: %LINEPROTO-5-UPDOWN: Line protocol on Interface Vlan1, cha
nged state to up
*Apr 25 06:11:58.117: %TRACKING-5-STATE: 1 ip sla 1 reachability Down->Up
*Apr 25 06:11:58.185: %SYS-5-CONFIG_I: Configured from console by on vty0 (EEM:
easy-ipsla-up-tracker)
*Apr 25 06:11:58.193: %HA_EM-6-LOG: easy-ipsla-up-tracker: Object reachable (cmd
output:
Router#)
*Apr 25 06:12:00.169: %LINK-5-CHANGED: Interface FastEthernet0, changed state to
administratively down
Notes: <number>

## Slide 27
Further Work, Known issues
Connectivity Verification
Notes: <number>

## Slide 28: EASy Further Work
Support for the IP SLA ED in EEM 3
- to provide more granularity than simple object tracking. For example,
one could trigger the EEM policy when a certain number of failures
have occurred out of a total number of attempts.
Improving the timer ED efficiency
- could change timer ED to a syslog ED but syslog messages such
as “%TRACKING-5-STATE” are not available on platforms such as
the Cat6K
Known Caveat: specifying commands to run with quotes does not
work properly due to IOS issue CSCsx72374
Notes: <number>

## Slide 29
Notes: <number>